## Slide 1: Drought Frequency Analysis in Tlamacazapa, Guerrero, Mexico
Robin Lynch
Hydrology
April 29,2010

## Slide 2: Tlamacazapa, Guerrero
Remote mountain village
Extreme poverty
Water scarcity
Reliant on wells contaminated with arsenic
Source: Google Maps

## Slide 3: Previous Work
Concluded:
  Year round piped water possible…but
  Needs 10 meter high dam downstream
Source: Google Earth

## Slide 4: Assumptions:
Only used average rainfall between 2003-2007
Doesn’t take into account long term variability!
Chart: Average Rainfall (mm/month)
| January | February | March | April | May | June | July | August | September | October | November | December
Average | 0.52 | 8.2 | 8.532 | 7.984 | 83.776 | 222.388 | 183.496 | 211.808 | 188.656 | 87.876 | 19.52 | 0

## Slide 5: Drought Frequency Analysis
Determine how impacted Tlamcazapa is by droughts
Use SPI (Standardized Precipitation Index)
Assumes data is normally distributed
Source: (Hallack-Algeria 2005)

## Slide 6: Instituto Mexicano de Technologia del Agua (IMTA)
16 gaging stations
Within 25 kilometer radius of Tlama
Rainfall data between 1940-1998
Inconsistent years in each station

## Slide 7: First station
Source:
(McKee et al. 1993)

## Slide 8: Second Station
Whoa!!!

## Slide 9: Theissen Polygons
Cannot take average of SPI per year
Each gage’s SPI thrown off due to incomplete time span
Must use Theissen Polygons to choose Nearest Neighbor
For years when closest gage has no data, use nearest neighbor “hot decking” imputation procedure

## Slide 11: 60+ years of Data!
Data from 1940-2007
(1944,1946,1999-2002 missing)

## Slide 12: Check for Normality

## Slide 13: …It’s Kinda Normal

## Slide 14: SPI Values for Tlama: 1940-2007

## Slide 15: HEC-SSP
Only looks at probability of exceedence

## Slide 16: Probability Distribution Function

## Slide 17: Drought Magnitude
Chart: 
Source: (McKee et al. 1993)

## Slide 18: Recurrence Probability
P(SPI<0) = 0.5
P(SPI<-1)= 0.15
P(SPI<-1.5)= 0.1

## Slide 19: Drought Frequency of Tlama

## Slide 20: Future Work
Statistical regression to see the relationship between drought and arsenic levels
Make recommendations for reservoir planning using this drought frequency analysis