## Slide 1: Effects of Urbanization on the Onion Creek Watershed
Laura Gundlach

## Slide 2: Effects of Urbanization on the Hydrograph
Increased Impervious Cover and Improved Drainage Systems cause:
  Higher Peak Flows
  Shorter Lag Times
  Higher Total Runoff Volumes

## Slide 3: Other Effects of Urbanization…
Less Recharge of Aquifers
Water Quality Degrades
  Water running off of impervious areas, such as roads and parking lots, can contain a lot of contaminants, such as oil and garbage

## Slide 4: Project Goals
Quantify the effects of urbanization on a real hydrograph
  Create a working basin model in HEC-HMS
  Find the hydrograph for a given storm
  Modify the land use data to include more development
  Compare the new hydrograph to the control
Learn how to find data, use ArcGIS, and use HEC-HMS

## Slide 5: Onion Creek Watershed
Red indicates the intensity of impervious cover
From National Land Cover Database

## Slide 6: Why Onion Creek?
Readily Available Data
  CAPCOG
Coming Under Increasing Development Pressure
  Includes much of South Austin, Buda
  Lower end contains the Airport

## Slide 7: Defining the Level of Detail
Using data from NDHPlus – 187 catchments

## Slide 8: Defining the Level of Detail
Using 12 digit Hydrologic Unit Codes – 9 Subwatersheds containing Onion Creek

## Slide 9: HEC-HMS Development
Basin Model
  9 Subbasins
  6 Reaches
  7 Junctions
Meteorlogic Model
  SCS Storm
Control Specifications

## Slide 10: Subbasins
Baseflow
  Assumed none
    Limited Streamflow Gages in the Area
    Interested in the difference in the hydrographs
Transform Method
  SCS Unit Hydrograph
    Requires a Parameter of Lag Time = .8*Tc
?

## Slide 11: Time of Concentration
TxDot Hydraulic Design Manual Nomographs
  Overland Sheet Flow to Stream
  Stream Flow to Junction
Times are Additive

## Slide 12: Subbasins
Loss Method
  SCS Curve Number

## Slide 14: Routing
Muskingum Routing
  Assumed x = .2, average for natural streams
  Assumed K = Travel Time through reach
    Found each Reach Distance
    Assumed v = 2 ft/s
Easily Weakest Parameters in Model
  Could not back calculate parameters because gages do not exist at each outflow point

## Slide 15: Precipitation Model
NWS TP-40 Rainfall Depth (5.5”) for an SCS Type 3 Storm

## Slide 16: Control Specifications and… Go!
Impatiently Waiting…

## Slide 17: Worked!

## Slide 18: “Urbanizing” the Watershed
Chose to make projections about growth in Buda (Subbasin 14), in South Austin (12), and around the Airport (13)

## Slide 19
Modified the percentage of the area with specific land uses
Found a new “urbanized” curve number
Basin 12 (South Austin)

## Slide 20: “Future” Run

## Slide 21: Comparison of Results

## Slide 22: Junction 7 Hydrographs
Original
Urbanized
Junction 7

## Slide 23: Quantitative agree with Qualitative?
Assumptions from Slide Two - Increased Impervious Cover and Improved Drainage Systems cause:
  Higher Peak Flows
  Shorter Lag Times
  Higher Total Runoff Volumes
YES
YES
YES

## Slide 24: Conclusions
Quantitative results agreed with qualitative assumptions, but the effect was not as dramatic as I hoped
  Lag Time increased only by 1 hour 12 minutes
  Hardly a recognizable difference in hydrographs
To adequately route flows, coefficients should be back calculated
I wish I would have taken GIS in the fall.

## Slide 25: Still to do…
Write report
Take GIS in the fall

## Slide 26: Questions?
Electric Peak – Yellowstone National Park
Never to be urbanized…