## Slide 1: Evapotranspiration (ET) from Dedicated Energy Crops
Ashlynn Stillwell
CE394K.2: Surface Water Hydrology Spring 2010
5/4/10

## Slide 2: Outline
Increasing biofuels production
Methods of calculating ET
Results for Mead Irrigated site
CO2 from crops
Future work
Questions

## Slide 3: Increasing Biofuels Production
Energy Independence and Security Act (2007) mandates 36 Bgal/yr by 2022
General consensus that new land will be cultivated
Additional crops might lead to additional ET
[EISA, Schnoor et al., USDA]
[earthfirst.com]

## Slide 4: AmeriFlux Sites for Analysis
ARMS SGP Main
  Corn/soybeans rotation
  Lamont, OK
Fermi Agricultural
  Corn/soybeans rotation
  Winfield Township, IL
Mead Irrigated
  Continuous corn
  Mead, NE
Rosemount G19 Alternative
  Corn/soybeans rotation
  Rosemount, MN
[AmeriFlux]

## Slide 5: Methods of Calculating ET
Reference ET0 (Penman-Monteith equation)
  ET0 for well-watered grass
  Kc crop factors adjust to ET
FAO CROPWAT 8.0 software
Energy balance method
Scaling of latent heat flux (using eddy covariance instruments)

## Slide 6: Penman-Monteith equation
Net radiation
Soil heat flux
Air temperature
Wind speed
Vapor pressure deficit
Slope of vapor pressure curve
Psychrometric constant
Pressure
Reference evapotranspiration ET0
Crop factors Kc

## Slide 7: ET Variation throughout Day
Chart: Crop Evapotranspiration (P-M) for Day 204 Mead Irrigated | 2005 corn crop | near Mead, NE
| 0 | 4.1666666666666664E-2 | 8.3333333333333315E-2 | 0.125 | 0.16666666666666696 | 0.20833333333333304 | 0.25 | 0.29166666666666707 | 0.33333333333333298 | 0.37500000000000006 | 0.41666666666666707 | 0.45833333333333293 | 0.5 | 0.54166666666666696 | 0.58333333333333293 | 0.62500000000000011 | 0.66666666666666707 | 0.70833333333333304 | 0.75000000000000011 | 0.79166666666666696 | 0.83333333333333304 | 0.87500000000000011 | 0.91666666666666696 | 0.95833333333333304
 | -0.13397 | -0.31964 | -0.10117 | 0.29449 | 0.50092 | 0.73812 | 2.7964 | 7.044 | 11.7041 | 15.963 | 19.7879 | 23.177 | 24.9535 | 25.3623 | 24.4568 | 22.2915 | 18.366 | 12.4905 | 7.635 | 2.7746 | 2.1971 | 1.7368 | 1.9656 | 2.5339

## Slide 8: FAO CROPWAT 8.0 software
Input data
  Climate
  Precipitation
  Crop (some built-in)
  Soil (some built-in)
Output: Crop Water Requirements

## Slide 9: Energy Balance / Scaling of Latent Heat
Energy balance method
Scaling of latent heat flux (when measured directly with eddy covariance instruments)
[Tanner]
[Hyun]

## Slide 10: Comparison of ET Methods
Chart: Mead Irrigated - Evapotranspiration Corn Crop 2005

## Slide 11: Cumulative ET for Methods
ET Calculation Method | Cumulative ET (mm) | Percent Error
Reference ET0 | 1,089 | 66%
Penman-Monteith | 707 | 8%
FAO CROPWAT software | 770 | 17%
Energy Balance (Tanner) | 824 | 26%
Scaling Latent Heat Flux | 656 | baseline
Indirect calculations overestimate ET compared to direct measurements

## Slide 12: CO2 from Crop Cultivation
Crop growing season
Chart: Mead Irrigated - CO2 Concentration Corn Crop 2005
No statistical difference between pre- and post-growth CO2

## Slide 13: Conclusions
Direct measurement of latent heat flux provides lowest magnitude of ET
Penman-Monteith equation with Kc provides good approximation
Crops sequester CO2, but other operations emit CO2
(Not shown here; in paper)
  Highest ET at ARMS SGP Main site (Oklahoma)
  Comparable ET from corn vs. soybeans

## Slide 14: Future Work
Write report
Beyond CE394K.2
  Satellite- and GIS-based methods of calculating ET
  Change from native vegetation to energy fuel crop

## Slide 15: Questions?
Data Acknowledgments
Office of Biological and Environmental Research of the U.S. Department of Energy as part of the Atmospheric Radiation Measurement Program
AmeriFlux Network, Oak Ridge National Laboratory