## Slide 1: The Sanderson Project
Finding the S vs. Q relationship
By: Cody Hudson
Notes: -Similar to HW7
-trying to find a relationship between storage and outflow so flow through the dam can be routed in HEC-HMS

## Slide 2: SITES Background
Water Resources “Site” Analysis Program
Developed for NRCS
Performs hydrologic and hydraulic analyses of water control structures
Calculates spillway stability

## Slide 3: Single Event Analysis
Used to simulate design storm through existing structures
Calculates
  Inflow Hydrograph
  Outflow Hydrograph
  Spillway Stability
  Storage/Outflow
Notes: -TR-60 does design of spillway elevation and material for large dams
-NHCP-378 does design of spillways for small dams less than 35 feet in height and with product of height (ft) and storage volume (acre-ft) less than 3,000

## Slide 4: Hydrology (Inflow)
Enter Rainfall or Hydrograph
Calculate SCS Hydrograph based on
  Basin characteristics
  Rainfall amount
  Rainfall distribution
Notes: -If you have a gage near the end of the basin you could use a hydrogaph
-Time of Concentration taken from previous NRCS study
-Curve number originally calculated in NRCS study but a different number was determined because of new research at Texas Tech (authors suggested taking calculated CN and subtracting 20 or using Antecedent Moisture Condition (AMC I)
-TR-55 gives storm rainfall and distribution for Eastern United States

## Slide 5: Elevation-Storage
E(S)=Elevation function of storage
dE(S)

## Slide 6: Hydraulics(Outflow)
Principal Spillway
  Orifice flow
  Weir flow
L
W
D

## Slide 7: Hydraulics (Outflow)
Auxiliary Spillway
  Open Channel Flow
  Width
  Side Slope
  Channel Slope
  Length
  Manning’s n
Notes: -Area (A) and hydraulic radius (R) are functions of water depth (H)

## Slide 8: Watershed Schematic
Structure
Reach
Uncontrolled
Subwatershed
Junction
Notes: -Graphical user interface similar to HEC-HMS
-Four different elements
-Reaches are used to perform river routing
-Structures have an associated subwatershed (Hydrology and Hydraulic Input screens)
-Uncontrolled subwatersheds (hydrology input screen only)
-Junction used to combine hydrographs

## Slide 9: Sites Model
CN=60
6hr 100 year rainfall = 5.11 in
Peak Flow = 10,323 cfs @ 8.6 hr
Notes: -6 hr rainfall taken from 1981 NRCS study
-CN=60 was selected based on SCS AMCI

## Slide 10: Sites Model
CN=74
6hr 100 year rainfall = 5.11 in
Peak Flow = 18590 cfs @ 6.5 hr

## Slide 11: Site 11
Notes: -after running model output text files for each structure are generated

## Slide 12: Questions