## Slide 1
Flood Prediction Partnerships in Texas
Public Private Partnerships in the Water Community:
Opportunities, Challenges and Next Steps Panel Discussion American Meteorological Society Annual Meeting, Denver, 11 January 2023
Presented by
David R. Maidment
Center for Water and the Environment
University of Texas at Austin
Acknowledgments: Texas Department of Transportation, Texas Division of Emergency Management Colleagues at UT Austin Center for Water and the Environment, USGS, ESRI, KISTERS

## Slide 2: Goals of the National Flood Interoperability Experiment (2015)
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 3: 787 traditional USGS gages now supplemented by 80 TxDOT Bridge RQ-30 radar sensors
USGS Traditional Gage
TxDOT Radar Sensor
Largest research project ever funded by TxDOT
Radar Streamflow Measurement at TxDOT Bridges
Notes: In Texas, the USGS operates 787 stream gages, 80 of which are part of this project.
Putting into perspective

## Slide 4
Measurement of Water Elevation and Velocity using RQ-30 Radar Gage
TxDOT has the largest network of RQ-30’s in the United States
These gages produce discharge measurements directly
without needing a rating curve
Disharge Computation:
Q = Vm * A(h)

## Slide 5: National Water Model (NWM) and National Bridge Inventory (NBI)
Chart: Number of Bridges
| US National Bridge Inventory | Bridges over Water | Bridges Predicted by NWM | Predicted by NWM in Texas
 | 619622 | 512925 | 443931 | 30073
100%
85%
72%
5%
NBI contains bridges
over 20 ft in length
Radar gaging on bridges could be scaled across the country

## Slide 6: NWC Flood Inundation Map Services are based on …
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Height Above Nearest Drainage (HAND)

## Slide 7
Cell Phone App for Observational Flood Mapping

## Slide 8: Pin2Flood Dashboard for Emergency Operations Center
Statewide deployment
in Texas in 2023

## Slide 9: Field Verification for River Forecasters
Close the gap between National Flood Forecasting and Local Flood Emergency Response
National
Local
Greg Waller
West Gulf River Forecast Center
Predictive
Flood
Mapping
Observational
Flood
Mapping
Chief Todd Pomroy
Austin Fire Department

## Slide 10: Conclusion
National
Local
USGS Traditional Gage TxDOT Radar Sensor
Public private partnerships lead to national prediction being supported by local observation