## Slide 1: GIS in Water Resources Midterm Review 2011
David Maidment, David Tarboton and Ayse Irmak

## Slide 2: Readings
Georeferencing and Coordinate Systems (Level 3) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#//00v20000000q000000.htm
Map Projections (Level 4) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_map_projections/003r00000001000000/ )
Geographic information Elements: (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/00v2/00v200000003000000.htm up to "Example: Representing surfaces"
Raster Data (Level 3) http://help.arcgis.com/en/arcgisdesktop/10.0/help/009t/009t00000002000000.htm Raster and Images, starting from "What is raster data" to end of "Raster dataset attribute tables" in "Fundamentals of raster data"
Slope http://www.ce.utexas.edu/prof/maidment/giswr2011/docs/Slope.pdf . (Level 4)
Hydrology tools (Level 5) http://help.arcgis.com/en/arcgisdesktop/10.0/help/009z/009z0000004w000000.htm to end of Hydrologic analysis sample applications in the Hydrology toolset concepts
Geometric Networks (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_geometric_networks/002r00000001000000/
Linear Referencing (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_is_linear_referencing/003900000001000000/

## Slide 3: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data

## Slide 4: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data
Georeferencing and Coordinate Systems (Level 3) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#//00v20000000q000000.htm
Map Projections (Level 4) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_map_projections/003r00000001000000/ )

## Slide 5
Latitude and Longitude on a Spherical Earth
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 6: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 7
Length on Meridians and Parallels (Spherical Earth)
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 8
Example: What is the length of a 1º increment along
on a meridian and on a parallel at 30N, 90W?
Radius of the earth = 6370 km.
Solution:
A 1º angle has first to be converted to radians
p radians = 180 º, so 1º = p/180 = 3.1416/180 = 0.0175 radians
For the meridian, DL = Re Df = 6370 * 0.0175 = 111 km
For the parallel, DL = Re Dl Cos f
= 6370 * 0.0175 * Cos 30
= 96.5 km
Parallels converge as poles are approached

## Slide 9: Curved Earth Distance on a Spherical Earth
Shortest distance is along a “Great Circle” (from A to B)
A “Great Circle” is the intersection of a sphere with a plane going through its center.
3. Great circle distance is R, where R=6378.137 km2
X
Z
Y
•

A
B
Ref: Meyer, T.H. (2010), Introduction to Geometrical and Physical Geodesy, ESRI Press, Redlands, CA, p. 108

## Slide 10: Shape of the Earth
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles

## Slide 11: Ellipse
P
F2
O
F1
a
b
X
Z


An ellipse is defined by:
Focal length = 
Distance (F1, P, F2) is
constant for all points
on ellipse
When  = 0, ellipse = circle
For the earth:
Major axis, a = 6378 km
Minor axis, b = 6357 km
Flattening ratio, f = (a-b)/a
~ 1/300

## Slide 12: Ellipsoid or Spheroid Rotate an ellipse around an axis
O
X
Z
Y
a
a
b
Rotational axis

## Slide 13: Horizontal Earth Datums
An earth datum is defined by an ellipse and an axis of rotation
NAD27 (North American Datum of 1927) uses the Clarke (1866) ellipsoid on a non geocentric axis of rotation
NAD83 (NAD,1983) uses the GRS80 ellipsoid on a geocentric axis of rotation
WGS84 (World Geodetic System of 1984) uses GRS80, almost the same as NAD83

## Slide 14: Definition of Latitude, f
(1) Take a point S on the surface of the ellipsoid and define there the tangent plane, mn
(2) Define the line pq through S and normal to the
tangent plane
(3) Angle pqr which this line makes with the equatorial
plane is the latitude f, of point S
O
f
S
m
n
q
p
r

## Slide 15: Cutting Plane of a Meridian
P
Meridian
Equator
plane
Prime Meridian

## Slide 16: Definition of Longitude, l
0°E, W
90°W
(-90 °)
180°E, W
90°E
(+90 °)
-120°
-30°
-60°
-150°
30°
-60°
120°
150°
l
l = the angle between a cutting plane on the prime meridian
and the cutting plane on the meridian through the point, P
P

## Slide 17
Global Positioning Systems
Distance to four satellites gives (x,y,z)
Notes: If we then make a measurement from a third satellite and find that we're 13,000 miles from that one, that narrows our position down even further, to the two points where the 13,000 mile sphere cuts through the circle that's the intersection of the first two spheres.
So by ranging from three satellites we can narrow our position to just two points in space.
To decide which one is our true location we could make a fourth measurement. But usually one of the two points is a ridiculous answer (either too far from Earth or moving at an impossible velocity) and can be rejected without a measurement.
A fourth measurement does come in very handy for another reason however, but we'll tell you about that later

## Slide 18: Representations of the Earth
Earth surface
Ellipsoid
~ Sea surface
Geoid
Geoid is a surface of constant
gravitational potential

## Slide 19: Definition of Elevation
Elevation Z
•
P
z = zp
z = 0
Mean Sea level = Geoid
Land Surface
Elevation is measured from the Geoid

## Slide 20: Vertical Earth Datums
A vertical datum defines elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
The National Elevation Dataset is in the NAVD88 datum
Heights are “elevation above datum”

## Slide 21: Geodesy and Map Projections
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data

## Slide 22: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 23: Types of Projections
Conic (Albers Equal Area, Lambert Conformal Conic) - good for East-West land areas
Cylindrical (Transverse Mercator) - good for North-South land areas
Azimuthal (Lambert Azimuthal Equal Area) - good for global views

## Slide 24
Projections Preserve Some Earth Properties
Area - correct earth surface area (Albers Equal Area) important for mass balances
Shape - local angles are shown correctly (Lambert Conformal Conic)
Direction - all directions are shown correctly relative to the center (Lambert Azimuthal Equal Area)
Distance - preserved along particular lines
Some projections preserve two properties

## Slide 25: Web Mercator Projection used for cached basemaps

## Slide 26: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin

## Slide 27: State Plane Coordinate System
Defined for each State in the United States
East-West States (e.g. Texas) use Lambert Conformal Conic, North-South States (e.g. California) use Transverse Mercator
Texas has five zones (North, North Central, Central, South Central, South) to give accurate representation
Greatest accuracy for local measurements

## Slide 28: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data
Geographic information Elements: (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/00v2/00v200000003000000.htm up to "Example: Representing surfaces"

## Slide 29
Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 30: Linking Geography and Attributes
GIS has a one to one association between a geographic feature and a record in an attribute table.
Geographic coordinates
Tabular attributes

## Slide 31
Themes or Data Layers
Vector data: point, line or polygon features
How each of these features could be represented using vector or raster?

## Slide 32
Image: Michael Zeiler, ESRI
Common Geospatial Information Types

## Slide 33
Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells

## Slide 34: Geodatabase – a store for all types of geospatial information

## Slide 35
ArcGIS Geodatabase (what is in a geodatabase)
Geodatabase
Feature Dataset
Feature Class
Geometric
Network
Object Class
Relationship
Workspace

## Slide 36
Geodesy, Map Projections and Coordinate Systems
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data
Spatial Reference = Datum + Projection + Coordinate system

## Slide 37: ArcGIS Spatial Reference Frames
Defined for a feature dataset in ArcCatalog
XY Coordinate System
  Projected
  Geographic
Z Coordinate system
Tolerance
Resolution
M Domain

## Slide 38: Horizontal Coordinate Systems
Geographic coordinates (decimal degrees)
Projected coordinates (length units, ft or meters)

## Slide 39: Key ArcGIS Software Components
ArcMap
ArcCatalog
ArcToolbox
Extensions
Geoprocessing

## Slide 40: Arc Catalog
View data
(like Windows Explorer)
Graphical
previews
Metadata
Tables

## Slide 41: Arc Toolbox
Map Projections
Tools for commonly used tasks

## Slide 42: Spatial Analyst
Analysis of land surface terrain as a grid
Key means of defining drainage areas and connectivity to stream network

## Slide 43: Geo-Processing
Toolbox tools linked together using the model builder to automate data processing

## Slide 44: Web-centered GIS
ArcGIS
Online

## Slide 45: An Integrated Systems Approach
ArcGIS
Online
ArcGIS Desktop
ArcGIS
Server

## Slide 47: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data
Raster Data (Level 3) http://help.arcgis.com/en/arcgisdesktop/10.0/help/009t/009t00000002000000.htm Raster and Images, starting from "What is raster data" to end of "Raster dataset attribute tables" in "Fundamentals of raster data"
Slope http://www.ce.utexas.edu/prof/maidment/giswr2011/docs/Slope.pdf . (Level 4)
Hydrology tools (Level 5) http://help.arcgis.com/en/arcgisdesktop/10.0/help/009z/009z0000004w000000.htm to end of Hydrologic analysis sample applications in the Hydrology toolset concepts

## Slide 48
x
y
f(x,y)
Two fundamental ways of representing geography are discrete objects and fields.
The discrete object view represents the real world as objects with well defined boundaries in empty space.
The field view represents the real world as a finite number of variables, each one defined at each possible position.
(x1,y1)
Points
Lines
Polygons
Continuous surface
Spatial Analysis Using Grids

## Slide 49
Numerical representation of a spatial surface (field)
Grid
TIN
Contour and flowline

## Slide 50
Grid Datasets
Cellular-based data structure composed of square cells of equal size arranged in rows and columns.
The grid cell size and extent (number of rows and columns), as well as the value at each cell have to be stored as part of the grid definition.
Number of columns
Number of rows
Cell size

## Slide 51
Raster Calculator
Cell by cell evaluation of mathematical functions

## Slide 52
Nearest Neighbor Resampling with Cellsize Maximum of Inputs
40
50
55
43
47
41
44
42
42
100 m
4
2
4
6
150 m
40-0.5*4 = 38
55-0.5*6 = 52
38
52
41
39
42-0.5*2 = 41
41-0.5*4 = 39

## Slide 53
Topographic Slope
Defined or represented by one of the following
  Surface derivative z
  Vector with x and y components
  Vector with magnitude (slope) and direction (aspect)

## Slide 54
DEM Based Watershed and Stream Network Delineation Steps
DEM Reconditioning/Burning in Streams
Fill Sinks
Eight direction pour point model to evaluate flow directions
Flow accumulation
Threshold stream network definition
Stream segmentation
Watershed delineation
Raster to vector conversion of streams and watersheds

## Slide 55
Filling in the Pits
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are filled they become sinks and isolate portions of the watershed
Pit filling is first thing done with a DEM

## Slide 56: Identifying and Removing Pits/Sinks in a DEM
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 6 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 6 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 9 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 9 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 9 | 9 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 9 | 9 | 9 | 9 | 15 | 15 | 12 | 15 | 15
15 | 9 | 9 | 9 | 9 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
Contains pits
Filled
A pit is a set of one or more cells which has no downstream cells around it.

## Slide 57
67
56
49
52
48
37
58
55
22
30
67
56
49
52
48
37
58
55
22
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent

## Slide 58
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water flows in the direction of steepest descent

## Slide 59
Flow Accumulation Grid.
Area draining in to a grid cell
ArcHydro Page 72
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Flow Accumulation > Threshold

## Slide 60
Watershed Draining to Outlet

## Slide 61
Stream links grid for the San Marcos subbasin
172
201
204
202
206
203
209
Each link has a unique identifying number

## Slide 62
Same Cell Value
Catchments for Stream Links

## Slide 63: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data
Geometric Networks (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_geometric_networks/002r00000001000000/
Linear Referencing (Level 2) http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_is_linear_referencing/003900000001000000/

## Slide 64
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams

## Slide 65
Raster Zones and Vector Polygons
Catchment Grid_code
Vector Polygons
Raster pixel value
Raster Zones
3
4
5
One to one connection

## Slide 66: Relationship
A relationship is an association or link between two objects in a database.
A relationship can exist between spatial objects (features in feature classes), non-spatial objects (objects in object classes), or between spatial and non-spatial objects.

## Slide 67: Relationship
Relationship between non-spatial objects
Water
Quality
Data
Water
Quality
Parameters

## Slide 68: Relationship
Relationship between spatial and non-spatial objects
Water quality data
(non-spatial)
Measurement station
(spatial)

## Slide 69
Relationships linking Catchments and Drainage Lines

## Slide 70: Zonal Average of Raster over Subwatershed joined to Subwatershed table
Join

## Slide 71
Catchment, Watershed, Subwatershed.
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 72
Network Definition
A network is a set of edges and junctions that are topologically connected to each other.
Hydro Networks in GIS

## Slide 73
Edges and Junctions
Simple feature classes: points and lines
Network feature classes: junctions and edges
Edges can be
  Simple: one attribute record for a single edge
  Complex: one attribute record for several edges in a linear sequence
A single edge cannot be branched
No!!

## Slide 74
Connectivity Table
J124
J125
J123
J126
E1
E3
E2
J123 | J124, E1 |  | 
J124 | J123, E1 | J125, E2 | J126, E3
J125 | J124, E2 |  | 
J126 | J124, E3 |  | 
Junction
Adjacent Junction and Edge
This is the “Logical Network”
p. 132 of Modeling our World

## Slide 75
Network Tracing on the Guadalupe Basin

## Slide 76: Linear Referencing
Where are we on a line?

## Slide 77
National Hydro Data Programs
National Elevation Dataset
(NED)
National Hydrography Dataset
(NHD)
Watershed Boundary Dataset
NED-Hydrology
Data Sources for GIS in Water Resources
What is it?
What does it contain?
What is the GIS format?
Where would it be obtained

## Slide 78: National River Network for Australia
Line flows to Line
Geometric Network
Geometry model: Where am I? (x,y coordinates)
Logical model: Who am I connected to? (topology)
Addressing model: Where are things on me? (linear referencing)
Image: Elizabeth McDonald, BoM

## Slide 79: Reach Catchments Every stream reach has a local drainage area
Area flows to Line
Fundamental connection between the water and land systems
Image: Elizabeth McDonald, BoM

## Slide 80: A challenge: those messy Aussie rivers have lots of loops and branches
Image: Michael Hutchinson, ANU

## Slide 81: Four Key Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 82: Cell Flows to a Cell
Core concept of flow on digital elevation models

## Slide 83: Line Flows to a Line
Geometric Network of NHDFlowlines

## Slide 84: Area Flows to a Line
Reach Catchments from NHDPlus
Flowline and Catchment have the same COMID

## Slide 85: Area Flows to a Point on a Line
Watersheds for USGS Gages