## Slide 1: ArcGIS Mapping of the Six Basins Groundwater Basin in Claremont, CA
Nicholas Brethorst
CE394K.3 GIS in Water Resources
Dr. Maidment, Fall 2012

## Slide 2: The Water Supply Problems
California Aqueduct
(State Water Project)
9 billion gallons per day
10% Supply Cut
Colorado River
Aqueduct
1.2 billion gallons per day
30% Supply Cut
Imported Water Supply in 2009
Saving the Delta Smelt is apparently more important than providing water to 24 million people.
Thank you Northern California
tree-hugging hippies!!!
(Three Valleys Municipal Water District, 2012)
Delta Smelt Fish (Google Images, 2012)

## Slide 3
Metropolitan Water District
of Southern California
Service Area
Three Valleys MWD
Largest Water District in USA
5,200 square mile service area
1.7 billion gallons per day
24 million people (and growing)

## Slide 4: Six Basins
Six Basins
Located in Claremont, CA
  45 miles east of Los Angeles
Claremont is a:
- Tree-huggin’
- Whale-savin’
- Prius-drivin’
- Recycled grocery bag-usin’
Kind of a Town!
I love
you
tree!
Six Basins Groundwater Basin
(Google Images, 2012)
Project Objectives:
  Six Basins Storage Capacity
  GW Pumping Effects

## Slide 5: Six Basins Monitoring Wells
Record Static GW Elevations
  Radio Pulses (every 5 seconds)
  Transmitted to Three Valleys
  Compiled on Excel
  Added to ArcGIS
Chart: Water Levels at MW2 in Upper Claremont Heights Basin May 3, 2004 Through December 31, 2010 G.S. Elev. ~1,527.2
Six Basins Monitoring Wells
Monitoring Well
Monitoring Well Static Groundwater Elevation Time Series Hydrograph

## Slide 6: Six Basins Member Agencies
  City of La Verne
  City of Pomona
  City of Upland
  Golden State Water Company
  West End Consolidated Water Company
  San Antonio Water Company
  Three Valleys Municipal Water District
Well Name | State Well # | Latitude oN | Longitude oW | GSE (ft) | DTW Pump (ft) | DTW Static (ft) | Well Depth (ft) | Upper Screen Depth (ft) | Lower Screen Depth (ft)
Amherst | 1S08W06A03 | 34.117411 | -117.756047 | 1,219.0 | 116 | 105.0 | 162.0 | 112.0 | 135.0
Beech | 1S08W06A01 | 34.119056 | -117.753858 | 1,238.0 | 212.5 | 212.5 | 450.0 | 250.0 | 435.0
LV Heights 1 | 01S08W06A02 | 34.118133 | -117.749950 | 1,266.0 | 165.9 | 165.9 | 450.0 | 185.0 | 435.0
LV Heights 3 | 01S08W05B01 | 34.122331 | -117.739328 | 1,288.0 | 116 | 116.0 | 309.0 | 185.0 | 210.0
Lincoln | 01S08W07F01 | 34.101153 | -117.762147 | 1,078.0 | 110.1 | 110.1 | 309.0 | 150.0 | 210.0
Mills Tract | 01S08W07F02 | 34.101886 | -117.762781 | 1,080.0 | 112.1 | 112.1 | 309.0 | 150.0 | 210.0
Old Baldy | 01S08W07F03 | 34.102947 | -117.780281 | 1,040.0 | 65.1 | 65.1 | 162.0 | 112.0 | 135.0
La Verne Production Wells in Six Basins

## Slide 7: Six Basins Production Wells
TVMWD Production Well
Six Basins Production Well Locations

## Slide 8: Six Basins Production Wells
Thiessen Polygons Tool
  Determined GW Elevations
Month | ƩAk (ft2) | ƩGWESTAT-Ak (ft3) | ƩGWEPUMP-Ak (ft3) | GWESTAT (ft) | GWEPUMP (ft) | ∆GWE (ft)
January | 622,844,540 | 70,291,236,329 | 69,248,069,013 | 1,214.7 | 1,196.7 | 18.0
February | 622,844,540 | 70,342,823,699 | 69,394,224,565 | 1,215.6 | 1,199.2 | 16.4
March | 622,844,540 | 70,234,292,493 | 69,309,143,713 | 1,213.7 | 1,197.8 | 16.0
April | 622,844,540 | 70,168,207,401 | 69,058,396,599 | 1,212.6 | 1,193.4 | 19.2
May | 622,844,540 | 69,911,553,847 | 68,858,956,188 | 1,208.2 | 1,190.0 | 18.2
June | 622,844,540 | 69,732,120,645 | 68,697,562,235 | 1,205.1 | 1,187.2 | 17.9
July | 622,844,540 | 69,802,992,186 | 68,488,889,124 | 1,206.3 | 1,183.6 | 22.7
August | 622,844,540 | 69,825,560,860 | 68,309,478,276 | 1,206.7 | 1,180.5 | 26.2
September | 622,844,540 | 69,691,768,432 | 68,456,649,540 | 1,204.4 | 1,183.0 | 21.3
October | 622,844,540 | 69,890,083,934 | 68,784,028,980 | 1,207.8 | 1,188.7 | 19.1
November | 622,844,540 | 69,699,147,387 | 68,582,890,361 | 1,204.5 | 1,185.2 | 19.3
December | 622,844,540 | 69,877,084,175 | 69,098,720,353 | 1,207.6 | 1,194.1 | 13.5
Six Basins Wells -Thiessen Polygon Attribute Table
Thiessen Polygons Created Using ArcGIS in the Six Basins
Thiessen GWE Equations Used

## Slide 9: Six Basins Borelog Table
WellID | Monitoring Well | TopElev (ft) | BottomElev (ft) | Soil Material | SoilLayer
1 | MW #1 | 1,852.786 | 1,591.786 | Sand and Gravel | Younger Alluvium
1 | MW #1 | 1,591.786 | 1,411.786 | Sand | Younger Alluvium
1 | MW #1 | 1,411.786 | 1,405.786 | Silts and Clays | Semi Confining Unit
1 | MW #1 | 1,405.786 | 0.000 | Gravel and Bedrock | Bedrock
2 | MW #2 | 1,527.155 | 1,356.155 | Sand & Gravel | Younger Alluvium
2 | MW #2 | 1,356.155 | 1,239.155 | Sand | Older Alluvium
2 | MW #2 | 1,239.155 | 726.155 | Silts and Clays | Older Alluvium
2 | MW #2 | 726.155 | 0 | Gravel and Bedrock | Bedrock
3 | MW #3 | 1,228.759 | 877.759 | Sand & Gravel | Younger Alluvium
3 | MW #3 | 877.759 | 634.759 | Sand | Older Alluvium
3 | MW #3 | 634.759 | 517.759 | Silts and Clays | Older Alluvium
3 | MW #3 | 517.759 | 0 | Gravel and Bedrock | Bedrock
Borelog Table for MW-1, MW-2, MW-3
Borehole Profiles of MW-1, MW-2, MW-3
Borehole Points of MW-1, MW-2, MW-3

## Slide 10: Six Basins Production Wells
Six Basins 2D Soil Profile at Monitoring Wells
Average Weighted Porosity = 0.27

## Slide 11: Six Basins Storage Capacity
Month | GWESTAT (ft) | GWEPUMP (ft) | Six Basins Area (ft2) | Weighted Porosity | StorageSTAT (AF) | StoragePUMP (AF) | ∆Storage (AF)
January | 1,214.7 | 1,196.7 | 622,844,540.5 | 0.27 | 46,896 | 46,200 | 696
February | 1,215.6 | 1,199.2 | 622,844,540.5 | 0.27 | 46,930 | 46,297 | 633
March | 1,213.7 | 1,197.8 | 622,844,540.5 | 0.27 | 46,858 | 46,240 | 617
April | 1,212.6 | 1,193.4 | 622,844,540.5 | 0.27 | 46,814 | 46,073 | 740
May | 1,208.2 | 1,190.0 | 622,844,540.5 | 0.27 | 46,642 | 45,940 | 702
June | 1,205.1 | 1,187.2 | 622,844,540.5 | 0.27 | 46,523 | 45,832 | 690
July | 1,206.3 | 1,183.6 | 622,844,540.5 | 0.27 | 46,570 | 45,693 | 877
August | 1,206.7 | 1,180.5 | 622,844,540.5 | 0.27 | 46,585 | 45,574 | 1,011
September | 1,204.4 | 1,183.0 | 622,844,540.5 | 0.27 | 46,496 | 45,672 | 824
October | 1,207.8 | 1,188.7 | 622,844,540.5 | 0.27 | 46,628 | 45,890 | 738
November | 1,204.5 | 1,185.2 | 622,844,540.5 | 0.27 | 46,501 | 45,756 | 745
December | 1,207.6 | 1,194.1 | 622,844,541.5 | 0.27 | 46,619 | 46,100 | 519
 |  |  |  | Total = | 560,061 | 551,268 | 8,793
Storage Capacity
Equations Used
Six Basins Annual Storage Capacity

## Slide 12: Six Basins GWE Modeling
Kriging Bayesian Interpolation Tools
  Static & Pumping Groundwater Levels
  Repeated for every month
Groundwater Modeling
Static GWE (January 2010)
Groundwater Modeling
Pumping GWE (January 2010)

## Slide 13: Six Basins GWE Modeling
Kriging Bayesian Interpolation Tools
  Static & Pumping Groundwater Levels
  Repeated for every month
Groundwater Modeling
Static GWE (July 2010)
Groundwater Modeling
Pumping GWE (July 2010)

## Slide 14: Six Basins GWE Modeling
Kriging Bayesian Interpolation Tools
  Static & Pumping Groundwater Levels
  Repeated for every month
Groundwater Modeling
Static GWE (December 2010)
Groundwater Modeling
Pumping GWE (December 2010)

## Slide 15: Six Basins GWE Modeling Results

## Slide 16: Six Basins GWE Modeling Results
Greatest Static GWE Difference in Pomona Basin (Break 1)
Lowest Static GWE Difference in Upper CH Basin (Break 6)
2010 Monthly Groundwater Elevations Difference |  |  |  |  |  |  |  |  |  |  |  | 
Month | Break 1 (ft) |  | Break 2 (ft) |  | Break 3 (ft) |  | Break 4 (ft) |  | Break 5 (ft) |  | Break 6 (ft) | 
 | Low | High | Low | High | Low | High | Low | High | Low | High | Low | High
Jan | 70.5 | 35.4 | 35.4 | 37.5 | 37.5 | 34.0 | 34.0 | 28.2 | 28.2 | 25.4 | 25.4 | 0.9
Feb | 56.1 | 42.1 | 42.1 | 46.4 | 46.4 | 50.4 | 50.4 | 47.8 | 47.8 | 33.6 | 33.6 | 7.8
Mar | 55.0 | 24.3 | 24.3 | 28.4 | 28.4 | 32.0 | 32.0 | 33.7 | 33.7 | 28.4 | 28.4 | 0.8
Apr | 76.3 | 29.8 | 29.8 | 21.8 | 21.8 | 18.3 | 18.3 | 17.8 | 17.8 | 10.3 | 10.3 | 5.9
May | 94.2 | 11.4 | 11.4 | 7.1 | 7.1 | 7.7 | 7.7 | 5.3 | 5.3 | 1.1 | 1.1 | 16.2
Jun | 86.9 | 16.7 | 16.7 | 17.5 | 17.5 | 18.0 | 18.0 | 10.4 | 10.4 | 1.3 | 1.3 | 6.1
Jul | 73.2 | 26.0 | 26.0 | 28.5 | 28.5 | 41.1 | 41.1 | 35.6 | 35.6 | 28.6 | 28.6 | 4.5
Aug | 50.2 | 35.4 | 35.4 | 40.3 | 40.3 | 50.5 | 50.5 | 43.1 | 43.1 | 29.6 | 29.6 | 4.6
Sep | 48.4 | 31.0 | 31.0 | 26.8 | 26.8 | 32.6 | 32.6 | 26.6 | 26.6 | 24.7 | 24.7 | 17.3
Oct | 72.5 | 56.1 | 56.1 | 54.7 | 54.7 | 53.0 | 53.0 | 39.3 | 39.3 | 34.1 | 34.1 | 22.9
Nov | 119.0 | 56.1 | 56.1 | 72.6 | 72.6 | 72.1 | 72.1 | 40.7 | 40.7 | 1.5 | 1.5 | 7.4
Dec | 69.6 | 1.9 | 1.9 | 2.5 | 2.5 | 18.1 | 18.1 | 10.5 | 10.5 | 14.4 | 14.4 | 9.9
Groundwater Modeling
Static GWE (July 2010)

## Slide 17: Summary
Six Basins Parameters | Value
Six Basins Area | 622,844,540.5 ft2
Static GWE | ~1,200.0 ft
Pumping GWE | ~1,190.0 ft
Storage Capacity | 560,000 acre-ft
Weighted Porosity | 0.27
Greatest GWE Change | Pomona & Upper Claremont Heights Basins

## Slide 18: Questions?

## Slide 19: References
Three Valleys Municipal Water District. (2012). Six Basins Annual Report 2010.
<http://www.threevalleys.com/downloads.aspx?DloadTypeID=2>.
(September 23, 2012).
Google Maps. (2012). Tree Huggers. <www.google.com/search>. (December 1, 2012).
Google Maps. (2012). Delta Smelt. <www.google.com/search>.
(December 1, 2012).

## Slide 20: Definition of Porosity
Definition of Porosity
Porosity Equation

## Slide 21
Types of Water Sources

## Slide 22
Three Valleys Municipal Water District Service Area
Diamond Bar
Glendora
Claremont
Walnut
Pomona
San Dimas
Rowland Hgts
Covina
La Verne
133 square mile service area
25 MGD
600,000 people