## Slide 1: Spatial Analysis Using Grids
Continuous surfaces or spatial fields representation of geographical information
Grid data structure for representing numerical and categorical data
Map algebra raster calculations
Interpolation
Calculate slope on a raster using
  ArcGIS method based in finite differences
  D8 steepest single flow direction
  D steepest outward slope on grid centered triangular facets
Learning Objectives

## Slide 2: Readings – at http://resources.arcgis.com/en/help/
http://resources.arcgis.com/en/help/main/10.1/index.html#/What_is_raster_data/009t00000002000000/ Raster and Images, starting from "Introduction/What is raster data" to end of " Fundamentals of raster data/Raster dataset attribute tables"

## Slide 3: Readings – at http://resources.arcgis.com/
What is the ArcGIS Spatial Analyst extension http://resources.arcgis.com/en/help/main/10.1/index.html#/What_is_the_ArcGIS_Spatial_Analyst_extension/005900000001000000/

## Slide 4: Two fundamental ways of representing geography are discrete objects and fields.
x
y
f(x,y)
The discrete object view represents the real world as objects with well defined boundaries in empty space.
The field view represents the real world as a finite number of variables, each one defined at each possible position.
(x1,y1)
Points
Lines
Polygons
Continuous surface
Notes: DRM

## Slide 5: Numerical representation of a spatial surface (field)
Grid or Raster
TIN
Contour and flowline

## Slide 6: Six approximate representations of a field used in GIS
Regularly spaced sample points
Irregularly spaced sample points
Rectangular Cells
Irregularly shaped polygons
Triangulated Irregular Network (TIN)
Polylines/Contours
from Longley, P. A., M. F. Goodchild, D. J. Maguire and D. W. Rind, (2001), Geographic Information Systems and Science, Wiley, 454 p.

## Slide 7: Discrete (vector) and continuous (raster) data
Images from http://resources.arcgis.com/en/help/main/10.1/index.html#/Discrete_and_continuous_data/009t00000007000000/

## Slide 8: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 9: Raster and Vector are two methods of representing geographic data in GIS
Both represent different ways to encode and generalize geographic phenomena
Both can be used to code both fields and discrete objects
In practice a strong association between raster and fields and vector and discrete objects
Notes: DRM

## Slide 10: A grid defines geographic space as a mesh of identically-sized square cells. Each cell holds a numeric value that measures a geographic attribute (like elevation) for that unit of space.

## Slide 11: The grid data structure
Grid size is defined by extent, spacing and no data value information
  Number of rows, number of column
  Cell sizes (X and Y)
  Top, left , bottom and right coordinates
Grid values
  Real (floating decimal point)
  Integer (may have associated attribute table)
Number
of
rows
Number of Columns
(X,Y)
Cell size
NODATA cell

## Slide 12: Points as Cells

## Slide 13: Line as a Sequence of Cells

## Slide 14: Polygon as a Zone of Cells

## Slide 15: NODATA Cells

## Slide 16: Cell Networks

## Slide 17: Grid Zones

## Slide 18: Floating Point Grids
Continuous data surfaces using floating point or decimal numbers

## Slide 19: Value attribute table for categorical (integer) grid data
Attributes of grid zones

## Slide 20: Raster Sampling
from Michael F. Goodchild. (1997) Rasters, NCGIA Core Curriculum in GIScience, http://www.ncgia.ucsb.edu/giscc/units/u055/u055.html, posted October 23, 1997

## Slide 21: Cell size of raster data
From http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/Cell_size_of_raster_data/009t00000004000000/

## Slide 22: Raster Generalization
Central point rule
Largest share rule

## Slide 23: Map Algebra/Raster Calculation
Precipitation
-
Losses (Evaporation, Infiltration)
=
Runoff
5
2
2
3
2
4
3
3
7
6
5
6
-
=
Cell by cell evaluation of mathematical functions
Example

## Slide 24: Runoff generation processes
Infiltration excess overland flow
aka Horton overland flow
Partial area infiltration excess overland flow
Saturation excess overland flow
P
P
P
qr
qs
qo
P
P
P
qo
f
P
P
P
qo
f
f

## Slide 25: Runoff generation at a point depends on
Rainfall intensity or amount
Antecedent conditions
Soils and vegetation
Depth to water table (topography)
Time scale of interest
These vary spatially which suggests a spatial geographic approach to runoff estimation

## Slide 26: Cell based discharge mapping flow accumulation of generated runoff
Radar Precipitation grid
Soil and land use grid
Runoff grid from raster calculator operations implementing runoff generation formula’s
Accumulation of runoff within watersheds

## Slide 27: Raster calculation – some subtleties
Analysis extent
+
=
Analysis cell size
Analysis mask
Resampling or interpolation (and reprojection) of inputs to target extent, cell size, and projection within region defined by analysis mask

## Slide 28: Spatial Snowmelt Raster Calculation Example
40
50
55
43
47
41
44
42
42
100 m
100 m
4
2
4
6
150 m
150 m

## Slide 29: Lets Experiment with this in ArcGIS
temp.asc
ncols 2
nrows 2
xllcorner 0
yllcorner 0
cellsize 150
NODATA_value -9999
4 6
2 4
snow.asc
ncols 3
nrows 3
xllcorner 0
yllcorner 0
cellsize 100
NODATA_value -9999
40 50 55
42 47 43
42 44 41

## Slide 30: New depth calculation using Raster Calculator
“snow100” - 0.5 * “temp150”

## Slide 31: Example and Pixel Inspector

## Slide 32: The Result
38
52
41
39
Outputs are on 150 m grid.
How were values obtained ?

## Slide 33: Nearest Neighbor Resampling with Cellsize Maximum of Inputs
40
50
55
43
47
41
44
42
42
100 m
4
2
4
6
150 m
40-0.5*4 = 38
55-0.5*6 = 52
38
52
41
39
42-0.5*2 = 41
41-0.5*4 = 39

## Slide 34: Scale issues in interpretation of measurements and modeling results
The scale triplet
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.
a) Extent
b) Spacing
c) Support

## Slide 35
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.

## Slide 36: Use Environment Settings to control the scale of the output
Extent
Spacing & Support

## Slide 37: Raster Calculator “Evaluation” of “temp150”
4
6
2
4
6
2
4
4
4
4
6
Nearest neighbor to the E and S has been resampled to obtain a 100 m temperature grid.
2
4

## Slide 38: Resample to get consistent cell size
4
6
2
4
5
3
3
5
4
4
6
2
4

## Slide 39: Calculation with consistent 100 m cell size grid
Outputs are on 100 m grid as desired.
How were these values obtained ?
38
52
41
39
47.5
40.5
42.5
40.5
45
“snow100” - 0.5 * “temp100”

## Slide 40: 100 m cell size raster calculation
40
50
55
43
47
41
44
42
42
100 m
150 m
40-0.5*4 = 38
42-0.5*3 = 40.5
38
52
41
39
43-0.5*5 = 40.5
41-0.5*4 = 39
47.5
40.5
45
40.5
42.5
50-0.5*5 = 47.5
55-0.5*6 = 52
47-0.5*4 = 45
42-0.5*2 = 41
44-0.5*3 = 42.5
4
6
2
4
5
3
3
5
4
4
6
2
4

## Slide 41: What did we learn?
Raster calculator automatically uses nearest neighbor resampling
The scale (extent and cell size) can be set under options
What if we want to use some other form of interpolation?
From Point
  Natural Neighbor, IDW, Kriging, Spline, …
From Raster
  Resample (Nearest, Bilinear, Cubic)

## Slide 42: Interpolation
Estimate values between known values.
A set of spatial analyst functions that predict values for a surface from a limited number of sample points creating a continuous raster.
Apparent improvement in resolution may not be justified

## Slide 43: Interpolation methods
Nearest neighbor
Inverse distance weight
Bilinear interpolation
Kriging (best linear unbiased estimator)
Spline

## Slide 44: Nearest Neighbor “Thiessen” Polygon Interpolation
Spline Interpolation

## Slide 45: Interpolation Comparison
Grayson, R. and G. Blöschl, ed. (2000)

## Slide 46: Further Reading
Grayson, R. and G. Blöschl, ed. (2000), Spatial Patterns in Catchment Hydrology: Observations and Modelling, Cambridge University Press, Cambridge, 432 p.
Chapter 2. Spatial Observations and Interpolation
http://www.catchment.crc.org.au/special_publications1.html
Full text online at:

## Slide 47: Spatial Surfaces used in Hydrology
Elevation Surface — the ground surface elevation at each point

## Slide 48
3-D detail of the Tongue river at the WY/Mont border from LIDAR.
Roberto Gutierrez
University of Texas at Austin

## Slide 49: Topographic Slope
Defined or represented by one of the following
  Surface derivative z (dz/dx, dz/dy)
  Vector with x and y components (Sx, Sy)
  Vector with magnitude (slope) and direction (aspect) (S, )
See http://www.neng.usu.edu/cee/faculty/dtarb/giswr/2012/Slope.pdf

## Slide 50: ArcGIS “Slope” tool
a
b
c
d
e
f
g
h
i

## Slide 51: ArcGIS Aspect – the steepest downslope direction

## Slide 52
Example
30
80
74
63
69
67
56
60
52
48
a
b
c
d
e
f
g
h
i
145.2o

## Slide 53
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope (Flow Direction Tool)
- Direction of Steepest Descent
30

## Slide 54
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
ESRI Direction encoding

## Slide 55: Limitation due to 8 grid directions.
?

## Slide 56
The D Algorithm
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

## Slide 57
The D Algorithm
If 1 does not fit within the triangle the angle is chosen along the steepest edge or diagonal resulting in a slope and direction equivalent to D8


## Slide 58
D∞ Example
30
eo
e7
e8
14.9o
284.9o
80
74
63
69
67
56
60
52
48

## Slide 59: Summary Concepts
Grid (raster) data structures represent surfaces as an array of grid cells
Raster calculation involves algebraic like operations on grids
Interpolation and Generalization is an inherent part of the raster data representation

## Slide 60: Summary Concepts (2)
The elevation surface represented by a grid digital elevation model is used to derive surfaces representing other hydrologic variables of interest such as
  Slope
  Drainage area (more details in later classes)
  Watersheds and channel networks (more details in later classes)

## Slide 61: Summary Concepts (3)
The eight direction pour point model approximates the surface flow using eight discrete grid directions.
The D vector surface flow model approximates the surface flow as a flow vector from each grid cell apportioned between down slope grid cells.