## Slide 1
Green Infrastructure, Groundwater and the Sustainable City
Larry Band
University of North Carolina
Visiting Professor
Chinese Academy of Science

## Slide 2: Baltimore City and County under consent decree to reduce N, P, sediment export to Chesapeake Bay

## Slide 3: How can principles derived from natural ecosystems be applied to urban ecosystems?
The Baltimore Ecosystem Study
The Coweeta Hydrologic Lab
Otto, North Carolina

## Slide 4: New Urban Water Balance Piped supply/drainage augments inflow/outflow leaky pipes, irrigation, sewer inflow&infiltration (I&I)
Bhasker and Welty, 2012, Env. Eng. Sci.
GI opportunity?

## Slide 5: Green Infrastructure (GI)
Network of vegetated features designed to provide specific ecosystem services by promoting infiltration and evapotranspiration
  stormwater mitigation, nutrient retention, carbon sequestration micro-climate modification
  green roofs, rain gardens, swale drains, constructed wetlands, expanded or retained tree canopy, downspout disconnection, …
  alternative or complement to traditional (grey) infrastructure
What GI elements and network designs most closely enable ecohydrological processes that mitigate urban stormwater while providing community benefits?

## Slide 8: GI appropriate over a range of urban development: urban form and cultural preferences
Baisman Run
WS 263
Dead Run

## Slide 9
forest
Medium density suburban san sewer
Low density suburban septic
Medium-hi density residential/commercial san sewer

## Slide 10: N load from catchments with forest loads and areas subtracted

## Slide 11
Baisman Run: Low density residential catchment, lawns, streets, septic systems

## Slide 12: Urban impervious hydrology – W263 buried streams, dense pipe network
Ken Belt, BES, USFS

## Slide 13
(Courtesy of Janet Choate)
RHESSys:
Regional Hydro-Ecological Simulation System
Notes: Strata can be redefined any time

## Slide 14
Lawn inputs fertilizer, pesticides
Road inputs
Car parts; Zn, Cd, Cu Emissions: N, legacy Pb
Roads: PAHs, Ca, NaCl
Leaky water supply, sewers, septic systems
C,N, P from human waste;
Pharmaceuticals and personal care products
Building inputs
Roof: PHAs, Zn
Paint: Legacy Pb
Ca from concrete
Compacted fill
Soil
Saprolite
Fractured bedrock
Saprolite
Fractured bedrock
“Natural” critical zone
The urban critical zone
Figure 1. The natural and urban critical zones. In the urban critical zone, topsoil is replaced by compacted fill, sewers and other utilities pierce the subsurface creating preferential flow paths, and there are additional chemical inputs from the built environment.
NSF Critical Zone Network criticalzone.org

## Slide 15: Sanitary paradigm: centralized treated supply, rapid removal of storm and waste water Dense pipe networks for supply distribution, drainage some outdoor water use, more leakage
Ken Belt, BES, USFS

## Slide 16: Loss of low order streams, expansion of drainage density
Kaushal and Belt, 2012

## Slide 17: Current models use simple removal rates – no dynamics Chesapeake Bay Program Expert Committee

## Slide 18: Detention and infiltration paradigms

## Slide 19: Prairie pothole hydrogeology: Depression focused recharge
van der Kamp and Hayashi, 2009, Hydrogeology Journal

## Slide 20: Potential for SCM infrastructure to replace lost riparian ecosystem retention function

## Slide 21: Rain garden receiving parking lot runoff

## Slide 22: Urban rain garden stub outs: Impervious surface run-on infiltration and transpiration

## Slide 24
Ecohydrology models can improve understanding of residential stormwater management
But these models are data hungry
Data management is challenging
Scientific reproducibility is difficult to achieve
Challenges of distributed ecohydrology modeling
Brian Miles, UNC

## Slide 25
Geoinformatics driven ecohydrology approach to residential stormwater management
orkflow tools to improve data management and scientific reproducibility
onnectivity of residential rooftops to adjacent impervious surfaces
ain gardens built on residential parcels
Developing:
Using models to assess how:
affect stormwater fate and transport in urban ecosystems

## Slide 26
Manual workflows
Workflow tools
orkflow tools
Notes: Explain what pieces have been implemented as iRODS rules.
Explain what iRODS is.

## Slide 27
Brian Miles, UNC

## Slide 28
Brian Miles, UNC

## Slide 29
Brian Miles, UNC

## Slide 30
Brian Miles, UNC

## Slide 31
Dead Run 5 (DR5) watershed
Landcover | Area %
Impervious | 41.8
Tree | 31.2
Lawn | 27.1
Impervious cover | % total area
Other impervious | 15.2
Roads | 15.0
Residential roof | 6.4
Non-residential roof | 5.2
DR5
Brian Miles, UNC

## Slide 32
Roof downspout disconnection to specified rain garden placement

## Slide 33
Ecohydrologic model tracks distribution of moisture stores and flowpaths with enhanced run-on infiltration: Green – increased saturation overland flow
Dead Run (Baltimore) shows significantly larger increase in saturation overland flow than S. Ellerbe Ck

## Slide 34
Rooftop disconnection only: marginal decreases in peak flow, increases in baseflow
Needs to be coupled with soil/vegetation retrofit

## Slide 35: Web service for rewiring urban drainage
Jeff Heard, UNC

## Slide 36: Interactive GI design to incorporate residential input and predict urban ecosystem outcomes
Residential Preference
Expected ecohydrology outcomes
GI parameters -> RHESSys models

## Slide 37
GI system design for urban restoration and development
  very initial phase
  Requires geohydrologic and social context
  Integrated GI networks, not independent elements
Ecohydrology models for urban stormwater and other ecosystem services (urban heat island, aesthetics, habitat)
  Coupled ecosystem dynamics
  spatially distributed surface water and groundwater
Developing sustainable and effective GI requires improved geoinformatics to advance models, facilitate implementation, incorporate community input into GI design;
Summary statements:

## Slide 38
Software availability – Brian Miles
https://github.com/selimnairb/EcohydroLib
https://github.com/selimnairb/RHESSysWorkflows
https://github.com/selimnairb/RHESSysCalibrator
https://github.com/RHESSys/RHESSys
http://grass.osgeo.org/grass64/manuals/addons/r.findtheriver.html