## Slide 1: HydroShare: Advancing Collaboration through Hydrologic Data and Model Sharing
David Tarboton, Ray Idaszak, Jeffery Horsburgh, Dan Ames, Jon Goodall, Larry Band, Venkatesh Merwade, Alva Couch, Jennifer Arrigo, Rick Hooper, David Valentine, David Maidment, Jeff Heard, Pabitra Dash, Tian Gan, Tony Castronova, Stephen Jackson, Cuyler Frisby, Stephanie Mills, Brian Miles
http://www.hydroshare.org
OCI-1148453
OCI-1148090
2012-2017
USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts, Texas, Purdue, SDSC

## Slide 2: Outline
The need for better data access cyberinfrastructure
CUAHSI HIS Services-Oriented Architecture
  Standards for hydrologic data storage and exchange
  Catalog for data discovery
  Integration of information from multiple sources
HydroShare
  Collaborative data analysis and publication
  Collaborative integrated modeling
  Architecture (Resource Centric Paradigm)
  Resource Data Model
  Functionality (to be) developed

## Slide 3: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity

## Slide 4
What proportion of your research time do you spend on preparing or preprocessing data into appropriate forms needed for research purposes?
http://his.cuahsi.org/documents/HISStatusSept15.pdf
Chart: 
| < 10 % | 10-25 % | 25-50 % | 50-75 % | > 75 % None
 | 18.6 | 45.7 | 24.3 | 11.4 | 0
Notes: Surveys of the hydrology community have indicated that data gathering and preprocessing is an inordinate fraction of the time required for modeling and analysis
In hydrology most of the easy single site, single variable, low hanging fruit research problems are solved and advances in understanding and better predictions require
combining information from multiple sources,
sharing and collaboration
Easier access to advanced computational capability
Sustainability and reliability in software

## Slide 5: A digital divide
Big Data and HPC
Researchers
Experimentalists
Modelers
awk
grep
vi
#PBS -l nodes=4:ppn=8
mpiexec
chmod
#!/bin/bash
Do you have the access or know how to take advantage of advanced computing capability?
Gateways, Web Interfaces, Software services

## Slide 6
http://www.cuahsi.org
What is CUAHSI?
Support
EAR 0753521
(as of January 2013)
109 US University members
7 affiliate members
20 International affiliate members
3 corporate members
provides community and research support services to advance water research

## Slide 7: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 8
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Slide: Michael Piasecki, Drexel University
Notes: 8

## Slide 9
What CUAHSI HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Slide: Michael Piasecki, Drexel University
Notes: 9

## Slide 10: CUAHSI Hydrologic Information System: A Services-Oriented Architecture Based System for Sharing Hydrologic Data
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards

## Slide 11: HydroDesktop
Uses EPA WATERS Web, Mapping, and Database Services at http://www.epa.gov/waters/geoservices/index.html to delineate Watersheds
An open source
dotSpatial GIS based desktop client that supports discovery and analysis of hydrologic observations data
Notes: The service URLs that the HD tool uses are seen in http://hydrodesktop.codeplex.com/SourceControl/changeset/view/475b15a84bf4#Source%2fEPADelineation%2fCallWebService.cs The HD tool uses the Point Indexing Service to find the nearest NHD reach to where the user clicked. This returns a location on that reach. This point location is then used as input to the Navigation Delineation Service to get the watershed, and the Upstream/Downstream Service to get the river lines. The delineation service has two limitations: * It only works up to a certain distance upstream. I think we have it set to 100km. So for large watersheds (those with more than 100km of stream length upstream of where the user clicked), we don't get the most upstream portions of the watershed. * It doesn't delineate exactly to where the user clicked. It delineates to the endpoint of the NHD reach. (Can't remember if it is the clicked reach or the upstream reach -- try it and see.)

## Slide 12
Search last 22 years for all data in buffer around watershed

## Slide 13: Download and Plot the Data
Combining information from multiple sources

## Slide 14: Perform an analysis using R
At your fingertips
the full analysis capability of R
data from multiple sources
accessed from distributed (cloud) resources.
importance of interoperability

## Slide 15: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 16: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Physical earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 17: Data models capture the complexity of natural systems
NetCDF (Unidata) - A model for Continuous Space-Time data
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}
ArcHydro – A model for Discrete Space-Time Data
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue
Terrain Flow Data Model used to enrich the information content of a digital elevation model
CUAHSI Observations Data Model: What are the basic attributes to be associated with each single data value and how can these best be organized?

## Slide 18: What are the basic attributes to be associated with each single data value and how can these best be organized?
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value
Variable
Method
Quality Control Level
Sample Medium
Value Type
Data Type
Source/Organization
Units
Accuracy
Censoring
Qualifying comments
Location
Feature of interest
Latitude
Longitude
Site identifiers
DateTime
Interval (support)

## Slide 19: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.
Provides a common persistence model for data storage

## Slide 20: Discharge, Stage, Concentration and Daily Average Example

## Slide 21: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 22
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
e.g. Arc Hydro

## Slide 23: Importance of the Observations Data Model
Provides a common persistence model for observations data
Syntactic consistency (File types and formats)
Semantic consistency
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 24
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 24

## Slide 25
http://www.opengeospatial.org/standards/waterml
Open Geospatial Consortium Web Service Standards
This document is an OGC® Encoding Standard for the representation of hydrological observations data with a specific focus on time series structures.
These standards have been developed over the past 10 years …. by 400 companies and agencies ....

## Slide 26: CUAHSI HIS: A common window on water observations data for the United States unlike any that has existed before
Storage in a community data model
Publication from a server
Data access through internet-based services using consistent language and format
Tools for access and analysis
Discovery through thematic and geographic search functionality
Integrated modeling and analysis combining information from multiple sources
Server
Desktop
Catalog

## Slide 27: HydroShare
Enable more rapid advances in hydrologic understanding through collaborative data sharing, analysis and modeling
Data
Analysis
Models
http://www.hydroshare.org
OCI-1148453
OCI-1148090
USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts,, Texas, Purdue, SDSC

## Slide 28: What is (will) HydroShare (be)?
HydroShare will be a community collaboration website that enables users to easily discover and access data and models, retrieve them to a desktop computer or perform analyses in a distributed computing environment that includes grid, cloud, or high performance computing model instances as necessary.
Understanding will be advanced through the ability to integrate information from multiple sources.
Outcomes (data, results, models) can then be published as new resources that can be shared with collaborators.
Data
Analysis
Models
Our goal is to make sharing of hydrologic data and models as easy as sharing videos on YouTube or shopping on Amazon.

## Slide 29: CUAHSI HIS
Publishing data requires access to or setting up a HydroServer
Accessing data requires HydroDesktop
Generally limited to time series at a point
Server
Desktop
Catalog

## Slide 30: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
HydroServer (ODM)
1
2
Observe
Publish and Catalog
3
Discover and Analyze/Model (in Desktop or Cloud)
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 31
Observers and instruments
Data
Analysis
Models
Collaboration
Share the results (Data and Models)
HydroShare resource
store
4
Collaborative data analysis and publication use case
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 32: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
Group Collaboration using HydroShare
Preparation of a paper
5
6
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 33: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
Submittal of paper, review, archival of electronic paper with data, methods and workflow
7
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 34: Collaborative Integrated Modeling Use Case
Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs (EcoHydroLib, TauDEM, CyberGIS)
Preconfigured models and modeling systems as services (SWATShare)
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for visualization and analysis
x
y
t
Flow
Time
Flow
Time
Time
P
Pre-processing and model linking
Modeling Services (e.g. SWATShare)
Notes: Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs
Preconfigured models and modeling systems as services
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for Visualization and Analysis
Automated reasoning to couple models based on purpose, context, data and resources

## Slide 35: Resource Repository Centric Paradigm for Modeling and Analysis
Analysis Tools
Visualization Tools
Data Loaders
Data Discovery Tools
Models
Resource Repository
Each model interacts with information in the common data store
The modeler does not need to be concerned with and can take advantage of standardized analysis, visualization loading and discovery tools
Enable multiple models to use common “best practice” tools

## Slide 36: Resource Data Model
Open Archives Initiative – Object Reuse and Exchange (OAI-ORE) - standards for the description and exchange of aggregations of Web resources
BagIt – hierarchical file packaging format designed to support disk-based or network-based storage and transfer of generalized digital content
Compatible with DataOne

## Slide 37: Definition of Data
In OMB Circular A-110 research data is defined as “recorded factual material commonly accepted in the scientific community as necessary to validate research findings, but not any of the following: preliminary analyses, drafts of scientific papers, plans for future research, peer reviews, or communications with colleagues.”
Validating research findings may involve
Observations and measurements
Models, code and scripts
Simulation results
HydroShare resources need to accommodate all these types of “data”

## Slide 38: Types of data to support as resources
Resource Types
Generic 
Time Series (CUAHSI HIS)
Geographic feature set
Geographic Raster
Referenced HIS time series
Multidimensional Space Time dataset
River geometry
Sample based observations (ODM2 and CZO)
Documents
Tabular objects
HydroDesktop Project package
Scripts
Models
Model Components
Referenced data sets from other (non HIS) sources.
Tools
Uploaders to facilitate loading of resources
Viewers to visualize the resource
Exporters to download the resource
Best practice tools for hydrologic data preprocessing and analysis
Resource Data Model.
Data and metadata content
Logical relationships
File formats

## Slide 41: Sharing and collaboration

## Slide 42: Architecture
Users
Browser
Client (HydroDesktop)
iRODS “Network File System”
Content
Resource Files
Resource Science Metadata
User Accounts
Functionality
Authentication and Authorization Infrastructure (AAI) for Access Control
Discovery (via Elastic Search / SOLR)
Web Pages
Web Services (HydroShare REST API)
Django web application framework
Web Tools
iRODS Native REST API
3rd party clients, interoperable systems and web tools
Connection point for partners
BiG CZ SSI
CI-WATER
SEAD
CyberGIS

## Slide 43: Django Web Application Architecture
Web Pages
Internal API
REST API
Model (Object classes specified in models.py)
Single point of truth for the format of resource types
Encodes resource data model
Schema (SQL generated from models.py)
Database (PostGIS)
Single point of truth for system and social metadata
Holds reflected science metadata
iRODS (Resources, Users, Authentication and Authorization Infrastructure)
Single point of truth for resources and their science metadata
Reflector to validate and parse science metadata from iRODS into Django
Loader to generate science metadata from user entry based on Resource Model Schema

## Slide 44
Top Menu
Home
My Resources
Discover
Collaborate
Support
Sign in
Page Architecture
Home
Hydroshare.org landing page
Sign up for new users
My Resources
Landing pages after login
Filtering
Listing of my resources and tagged resources
Discover
Implements search over all resources in HydroShare
Uses science metadata in iRODS
Collaborate
Implements discovery and joining of groups
Support
Help and tutorial pages
Sign in
Sign in
New account
Recovery
Resource landing page
Science metadata display (and editing)
Rapid visualization thumbnail
Social functionality (commenting, rating, tagging)
Sidebar with launch links for tools that can work on that resource
Tools (loosely coupled)
Not constrained to be within Django Framework
May be launched from any resource landing page
Access resources through REST API
Encouraged to use HydroShare “style” but not constrained by it
Can even be on separate platform with separate OS
Group landing page
Description
Membership
Joining and leaving
Activities

## Slide 45: Loose Integration of web tools
Not web app as “session object” is not shared
Access resources using “token” that identifies user for access control
Use mapping table in Django to associate tools with resource types and create launch links sidebar
Loosely coupled tool examples
  Geoanalytics for visualizing feature (shapefile)
  Geoanalytics for visualizing raster
  Time Series Analyst (from HydroServer) for visualizing time series
  A web viewer for NetCDF based on IDV

## Slide 46: iRODS
iRODS in HydroShare
Storage of HydroShare Resources Replicated across multiple institutions
Access to Computation
Access to Indexing for Discovery
Rule Engine
MSVC
R. Server
R. Server
…
Client
Users
iCAT
Distributed Data Grid Middleware:
Metadata Catalog holding virtual file system information and associated metadata
Extensible number of ‘Resource Servers’ which may provide connectivity to storage resources
Integrated Rule Engine for Policy Driven Data Management triggered by Data Management Activities
Extensibility via Microservices (MSVC) – Plugins providing functionality to the Rule Engine

## Slide 47: Summary
A new, web-based system for advancing model and data sharing
Sharing features to HydroDesktop
Access more types of hydrologic data using standards compliant data formats and interfaces
Enhance catalog functionality that broadens discovery functionality to different data types
New model sharing and discovery functionality
Facilitate and ease access to use of high performance computing
New social media and collaboration functionality
Links to other data and modeling systems

## Slide 48: Thanks to a lot of people
  USU
  RENCI/UNC
  CUAHSI
  BYU
  Tufts
  UVA
  Texas
  Purdue
  SDSC
http://hydroshare.cuahsi.org
OCI-1148453
OCI-1148090
Notes: The HydroShare project is part of a broad effort in CUAHSI in the area of Hydrologic Information Systems. We have a team of developers and domain scientists from eight universities working on HydroShare. This is part of the even broader focus in NSF on data management, Cyberinfrastructure and sustainable software.