## Slide 1: River flow routing using HydroSHEDS for North America
Wen-Ying Wu
Jackson School of Geosciences,
The University of Texas at Austin
Email: wenying@utexas.edu
2016.11.15

## Slide 2: Motivation-National Water Model
2.7 million rivers
Slide from Course of “GIS in Water Resources” by Dr. David Maidment

## Slide 3: Our Task- to apply it globally, but first try NA
Historical Runoff Data
HydroSHEDS river network
RAPID
Historical Stream Flow
Output of land surface model
Global converge, but first try NA
River network connectivity information
Inflow of surface and subsurface water to the river network
Some estimation of model parameters

## Slide 4: HydroSHEDS
HydroSHEDS
(Hydrological data and maps based on Shuttle Elevation Derivatives at multiple Scales)
  15sec GRID: Flow Direction
  15sec SHAPE: River Network
approx. 450 meters at the equator
About 46789 rivers in North America

## Slide 5: ArcGIS Toolbox for preprocessing river network
Toolbox | Geoprocessing | Purpose
ArcHydro | Generate From/to Node for Lines | Create connectivity of river by morphology
 | Find Next Downstream lines | 
GIS | Watershed | Define watershed for each stream line
 | Extract Value to Point | Find centroid for each watershed
 | Joint Netcdf for raster | 
 | Feature to Table | 
 | Feature to Raster | 
 | Raster to Polygon | 
 | Export Table to Excel | 
 | Polyline to raster | 
 | Join Field | 
 | Extract Value to Point | 

## Slide 6: Tool-Generate From/to Node for Lines Find Next Downstream lines
HydroID NextDownID
459944 459960
459960 460031
459961 460031
460031 460033
460058 459960
Create connectivity of river by morphology

## Slide 7: Tool-Watersheds, Feature to Point
Watersheds-Define watershed for each stream line(with flow direction)
Extract Value to Point-Find centroid for each watershed

## Slide 8: Runoff data
GLDAS Surface Runoff 2015.05.24 00z
Case: 2015. May Texas Flooding
Model run: 2015.05.15~2015.05.31
Runoff Data:
GLDAS 0.25 degree 3-hourly
(Including surface runoff and surface runoff)

## Slide 9: RAPID output- all streamline
2015.05.15
2015.05.31
Streamflow

## Slide 10: RAPID output-Animation

## Slide 11: RAPID output-Colorado River Basin
Chart: Colorado River Basin

## Slide 12: Future work
Evaluate the results with gage station
Longer time period
Other continent

## Slide 13
Thanks for listening!
Question?