## Slide 1: Grapevine Lake Modeling & Watershed Characteristics
Nash Mock

## Slide 2: Location & Background
Located between Tarrant and Denton counties in North Texas
Constructed following the Rivers & Harbors Act of 1945
Built 1948-1952 by the Army Corps of Engineers
Dallas/Fort Worth Metroplex flood control, water storage & recreational waters

## Slide 3: Digital Elevation Model and NHDPlus Streams
Elevation Range: 170-395 ft.
Watershed Area: 1799 km2
Lake Surface Area: 29.47 km2
Medium Resolution Reaches Draining to Grapevine Lake: 604
Total Reach Length: 1326 km

## Slide 4: Denton Creek
Largest GNIS stream draining to Grapevine Lake
Stream Length: 147 km
Discharge from dam joins the Elm Fork of Trinity River

## Slide 5: Reservoir Storage Timeline
Dead Pool | Conservation Pool | Flood Pool/ Emergency Spillway | Max Design Elevation | Top of Dam
475 ft. | 535 ft. | 560 ft. | 581.9 ft. | 588 ft.

## Slide 6: 2006-2016 Summer Drought History
Yellow: Abnormally Dry
Light Orange: Moderate Drought
Orange: Severe Drought
Dark Orange: Extreme Drought
Red: Exceptional Drought
2012-2014 corresponds to extended conservation pool period

## Slide 7: Watershed Flow Direction
Majority of flow east towards dam (purple)
Flow around dam directed north (light blue)
Anomalous around lake boundaries

## Slide 8: Watershed Land Slope
Land Slope Range: 0-71%
DEM indicates Grapevine Lake is nearly flat
Anomalous around lake boundaries

## Slide 9: Watershed Flow Accumulation
Flow accumulates along northern boundary of lake
Appears to jump from watershed above dam location
Anomalous around lake boundaries

## Slide 10: Grapevine Lake Contours
Lake Depth: 70 ft.
Contours from Texas Water Development Board 2011 lake survey
1, 2, 5, and 10 ft. contours up to conservation pool elevation

## Slide 11: Grapevine Lake Bathymetric Model
Used 2 ft. contours to assist rendering
Local scene view since earth’s curvature insignificant
Extruded contours down from conservation pool elevation
Scale and north direction not well represented in 3D

## Slide 12
Remaining Work
Perform a HAND analysis on the Grapevine Lake watershed.
Further improve bathymetric model by extruding polygons between contour polylines.

## Slide 13
Questions?