## Slide 1: Hydrologic Data Access Using Web Services
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Canadian Water Resources Association Conference
St John’s, Newfoundland, 28 June 2011

## Slide 2
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
http://www.cuahsi.org

## Slide 3: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 4: Services-Oriented Architecture for Water Data
Catalog
Server
User
Data access
Service registration
Search
Catalog harvest
WaterML – web language for water data

## Slide 5: WaterML as a Web Language
Discharge of the San Marcos River at Luling, TX June 28 - July 18, 2002
USGS Streamflow data in WaterML language
The USGS now publishes its time series data as WaterML web services

## Slide 6: Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060
I accessed this WaterML service from USGS at 9PM last night
And got back these flow data from USGS which are up to 8PM Central time

## Slide 7: CUAHSI Water Data Services Catalog
66 public services
18,000 variables
1.9 million sites
23 million series
5.1 billion data values
And growing
The largest water data catalog in the world
maintained at the San Diego Supercomputer Center

## Slide 8: Point Observations Information Model
Data Source
Network
Sites
Variables
Values
{Value, Time, Metadata}
Niagara Peninsula Conservation Authority
Water Quality
BA001
Total Phosphorus
0.89 mg/L, 20 April 2009
A data source operates an observation network
A network is a set of observation sites
A site is a point location where one or more variables are measured
A variable is a property describing the flow or quality of water
A value is an observation of a variable at a particular time
A metadata quantity provides additional information about the value
GetSites
GetSiteInfo
GetVariableInfo
GetValues
Information is transmitted through the internet in WaterML as web services

## Slide 9: Niagara Peninsula Conservation Authority
71 Observation sites
76 water quality variables
3797 time series
148, 693 data values
http://www.his.npca.ca/waterdataservices_quality/cuahsi_1_1.asmx?WSDL

## Slide 10: HydroDesktop – Desktop HIS
Metadata
Data
Catalog

## Slide 11: Three Categories of Data Services
Data Services – which convey the data
Metadata Services – which convey metadata about specific collections or series of data
Search Services – which enable search, discovery, and selection of data and convey metadata required for accessing data using data services
Data
Metadata
Search
Services
Search
Data
Metadata

## Slide 12: Open Geospatial Consortium Web Service Standards
Map Services
Web Map Service (WMS)
Web Feature Service (WFS)
Web Coverage Service (WCS)
Catalog Services for the Web (CS/W)
Observation Services
Observations and Measurements Model
Sensor Web Enablement (SWE)
Sensor Observation Service (SOS)

## Slide 13
Meets every 3 months
Teleconferences most weeks
WaterML Version 2 standard proposed
Vote for adoption later this year
Jointly with World Meteorological Organization
Evolving WaterML into an International Standard
November 2009
Hydrology, Meteorology, Climatology, and Oceanography

## Slide 14: OGC/WMO Hydrology Domain Working Group
This is now an accepted forum for international evolution of water data sharing standards
September 2011 OGC Technical Committee meeting in Boulder, CO, includes a “Hydrology Summit”
March 2012 OGC Technical Committee meeting will be in Austin, Texas

## Slide 15: Organize Water Data Into “Themes”
Integrating Water Data Services From Multiple Sources
. . . Across Groups of Organizations
WaterML
WaterML
WaterML
WaterML
WaterML

## Slide 16
Streamflow Data Services
2 services
7 variables
4,363 sites
11,484 series
9,493,968 records
Notes: Here’s an example showing where streamflow is measured in Texas from two different services (i.e., data providers).

## Slide 17
Water
Temperature Data Services
6 services
11 variables
11,158 sites
22,953 series
1,546,841 records

## Slide 18
Bacteria Data Services
1 service
21 variables
4,801 sites
15,483 series
297,849 records

## Slide 19: Tropical Storm Hermine, Sept 7-8, 2010

## Slide 20: Local Information during Tropical Storm Hermine (7-8 Sept 2010)
http://hydromet.lcra.org
http://coagis1.ci.austin.tx.us/website/COAViewer_fews/viewer.htm
http://ubcwcid.org/Overview/Overview.aspx?id=1
LCRA
City of Austin
Upper Brushy Creek (Round Rock)
TV
Bring data together into one system

## Slide 21: Real-Time Observations Map Layer
Real-Time WaterML service
Map Query Layer
Query Script to acquire observations
Output Map Layer for results
Output Map Service
Viewing System
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P1D&parameterCd=00065
Continually updating
http://129.116.104.176/PublicSafetyCOP/index.html
Stage Height Map Service (USGS and City of Austin) http://129.116.104.176/ArcGIS/rest/services/RealTime/COA_REALTIME/MapServer
NEXRAD Map Service http://129.116.104.176/ArcGIS/rest/services/RealTime/COA_NEXRAD/MapServer
Common Operating Picture Viewer:

## Slide 22: ESRI Public Safety Situational Awareness Viewer
Continuously updated maps of rainfall and stage height from multiple web services

## Slide 23: Web Services HUB
USGS
LCRA
NWS
COA
AHPS
Web Services HUB
Inputs
Observation
Data
Services
(WaterML)
Channel
Data
Services
(WFS)
Models
Modeling
Services
Data
Services
(WFS)
Mapping
Services
(WFS)
Maps
Outputs
Observation
Data
Services
(WaterML)
Mapping
Services
(WFS)

## Slide 24: Conclusions
Water web services are operational
There are three levels
  Publishing individual time series (USGS)
  Publish an observations network (NPCA)
  Publishing a collection of networks (Texas Water Development Board, CUAHSI)
Thematic maps can be built from time series
This is all supported and endorsed by WMO